## Slide 1
OnePagers and Land-use Sector
2050 Calculator
Onesmus Mwabonje
Paisan Sukpanit
Victoria Hoare
Jeremy Woods

## Slide 2: 8 step plan for 2050 KCERT success
Think about the drivers for sector
Draw up driver tree
Think about your draft 1 pager
Come up with your list of inputs
What will your stakeholder say?
Excel workbook and webtool Development
What insights can we get out of this?
Think about your stakeholder workshop

## Slide 3: Driver tree: What are the drivers for international aviation in the UK?
Key
= Output
= Inputs
Annual Emissions (kg CO2e)
Fuel consumed (kW h)
Emissions factor (kg / kW h)
Total person-distance flown (passenger-km)
Efficiency (kW h / passenger-km)
UK population
Average number of flights / year
Average distance per flight
(km)
Distance flown per person
(passenger-km)
×
×
×
×
Abiding principle. Don’t over complicate. If you can simplify, do.

## Slide 4: Driver tree: What are the drivers for solar PV in Kenya?
Key
= Output
= Inputs
Annual Electricity generated (TWh)
Total solar panels installed (sq m)
Efficiency factor
(%)
Average roof area (sq metre)
Number of roofs
×
×
Abiding principle. Don’t over complicate. If you can simplify, do.
Average sunlight
(W sq m)

## Slide 5: What does your 1-pager look like (write template)
Kenya has strong potential for solar projects and has already installed c15MW.
Level 1
Level 2
Level 3
Level 4

## Slide 6: What is this missing out or what are the broad assumptions
Assumes normal PV, rather than Concentrating Solar Power (CSP). But you can change that quite easily by varying the efficiency factor
That normal PV does not become more efficient in the future – again this can be changed, so check with your stakeholders
We assume zero emissions from the sector because any production based emissions would either be included elsewhere or would be in another country

## Slide 7: The inputs for the solar section of the KCERT 2050 Calculator
Input | 2013 | 2020 | 2030 | 2040 | 2050 | Comments
Efficiency factor (%) | 20% | - | - | - | 20% | Unlikely that Kenya will be able to influence the international market. But could get better anyway
Sunlight conversion factor (W/ m sq) | 220 | - | - | - | 220 | Unlikely to get any sunnier
Installed capacity (MW) | 15 | - | - | - | ? | Yes – this seems like the key driver that can really be driven by ambition from government and the private sector
Focus on present day and 2050 to begin with. You can change the linear trajectory later.

## Slide 8: Who to invite for your stakeholder workshop, and what to ask them?
From government:
From NGOs:
From business:
From academia:

## Slide 9: Example KCERT: one pager - Solar
Kenya has strong potential for solar projects (sun twice as powerful as in the UK). To date 15MW have been installed.
Level 1
Nothing more achieved other than the 15MW currently installed due to lack of government support and expensive PV panel prices.
Level 2
Current government ambition continues to 2050. Leading to 25GW installed capacity by 2050 providing 44 TWh per year. This would take up a land area of 113,000 sq km.
Level 3
Kenya doubles it’s current level of ambition, resulting in 50GW (88TWh per year).
Level 4
A huge effort is made, and 1.2m2 per person of Kenya is dedicated to solar PV. This delivers 175 TWh per year of electricity, through 100 GW of installed capacity. The IEA estimate total global installed capacity by 2050 to be 3000GW.
TWh per year
TWh per year
For some context – what other countries have assumed……..

## Slide 10: Example 1: one pager – Solar

## Slide 11: Example 2: One pager - Forestry

## Slide 12: Deep dive into the land, bioenergy and waste sectors

## Slide 13: Interlinkages
Bioenergy resources
Solid biomass
Liquid biomass
Biogas
Electricity generation
Land
Forests
Bioenergy land
Arable land
Livestock grazing land
Waste
Dry waste
Wet waste
Used cooking oil
Heat generation
Biofuels
Buildings
Transport
Industry

## Slide 14: Levers in this sector
Lever | Description
Farming Yield & Efficiency | Reductions in the number of livestock, crop yield improvements and the emission intensity of agricultural processes
Forestry | Land dedicated to planting forest (requires land to be freed up using the Farming Yield & Efficiency lever)
Land for Bioenergy | Land dedicated to growing bio-crops (requires land to be freed up using the Farming Yield & Efficiency lever)
Waste Reduction | Amount of waste produced, recycled and diverted to energy processes

## Slide 15: Livestock
Category | Bio resources | Greenhouse Gas Emission
Poultry | No | No
Cattle | Yes | Yes
Other | Yes | Yes

## Slide 16: Land Yield

## Slide 17: Land-Use Change Assumptions
Land Gain
Land Loss
Woodland
Bioenergy Land
Livestock Grazing Land
Arable Land for Food
UK assumptions to have fixed profile
Other Land
Settlements

## Slide 18: Calculation of land balance

## Slide 19: Calculation logic of land balance
BaU Scenario for land-use
Deductible land
New Forests
New Bioenergy land
Existing Forests
Existing Bioenergy land
Final Livestock grazing land
Final Arable land for food
Final Forests
Final Bioenergy land

## Slide 20: Bio Resource Availability

## Slide 21: Calculation logic – Bio resources
Forests
Wood
Collected for Energy
Arable Land for Food
Livestock
Straw
Manure
Leftover waste (Not collected for energy)

## Slide 22: Emissions

## Slide 23: The Waste Sector

## Slide 24: Calculation logic
Waste
Recycle
Energy from Waste
Landfill
Biogas captured from landfill
Biogas released to the atmosphere

## Slide 25: Emissions

## Slide 26: Discussions
UK Land-use categories | Kenya
Forests | 
Bioenergy land | 
Arable land for food | 
Livestock grazing land | 
Settlements | 
Other land | 

## Slide 27: Next steps
Team to familiarise with the spreadsheet model
Start considering and gathering data for each sector (Data tracker)
Continue identifying and mapping key sector stakeholders
Planning for co-design and expert sector workshops
Continue with deep-dive on sector logic trees (Transport and Industry sectors)
Start to think about One pagers development